## Slide 1: CS 1680 Intra-domain Routing
Based partly on lecture notes by Rodrigo Fonseca, David Mazières, Phil Levis, John Jannotti

## Slide 2: Administrivia
IP milestone meetings: Should meet with staff today
IP: Next steps
  Gearup II: see recording/notes
  See Implementation Start Guide, other resources
  Do not leave this project until the last minute
HW1 due tonight

## Slide 3
What is the destination MAC address when H1 is sending the following packets?
1.2.1.2
aa:aa:aa
1.2.1.1
cc:cc:cc
1.2.1.0/24
Warmup
Prefix | IF/Next hop
1.2.1.0/24 | IF1
0.0.0.0 | 1.2.1.1
 | Src | Dest
Link | aa:aa:aa | ???
IP | 1.2.1.2 | 1.2.1.1
H1
1.2.1.3
bb:bb:bb
H1’s forwarding table:
 | Src | Dest
Link | aa:aa:aa | ???
IP | 1.2.1.2 | 1.2.1.3
1)
2)
 | Src | Dest
Link | aa:aa:aa | ???
IP | 1.2.1.2 | 8.8.8.8 (Google)
3)
Notes: Let’s first look at how we move packets between the two networks

## Slide 4: Recap: IP vs. Link-layer address
 | Src | Dest
Link | aa:aa:aa | cc:cc:cc
IP | 1.2.1.2 | 8.8.8.8 (Google)
Link-layer header info (Ethernet/Wifi/etc)
- Destination MAC address is link-layer addr
for packet’s next hop
- Changes every hop
- Each hop could use a different link-layer
protocol!
IP header info
- Destination IP is IP address of packet’s final destination
- Routers look at destination IP to figure out where packet goes next (and which MAC address goes on packet next)

## Slide 5
Map of the Internet, 2021 (via BGP)
OPTE project

## Slide 6: What does this thing do?

## Slide 7: What we're still missing
… in order to make IP actually work in practice
=> How do you get an IP address? (DHCP)
=> What your home router does (NAT)
=> IPv6
We'll see the good, the bad, and the ugly...

## Slide 8: How do you get an IP address?

## Slide 9: Getting an IP
Two ways to configure an IP for a host:
Static configuration: manually specify IP address, mask, gateway, …
Automatic: ask the network for an IP when you connect!

## Slide 10: Getting an IP
Two ways to configure an IP for a host:
Static configuration: manually specify IP address, mask, gateway, …
=> More common with network devices that don’t change often
Automatic: ask the network for an IP when you connect!
    => Most common for end hosts
    => Dynamic Host Configuration Protocol (DHCP)

## Slide 11: DHCP: The idea
Dynamic Host Configuration Protocol

## Slide 12: DHCP: The idea
Dynamic Host Configuration Protocol
Every network has a “pool” of IPs it can assign to hosts
  Some subset of its prefix (eg. 192.168.1.0/24)
When a host connects, it asks a DHCP server for an address from the pool
DHCP server(s) act like allocators: give “leases” to IPs, provide other config info

## Slide 13
Host A
DHCP server

## Slide 14
Host A
Src: A's MAC address
Dst: ff:ff:ff:ff:ff:ff
DHCPDISCOVER
DHCP server
=> Again, host needs to use broadcast address. Why?
=> Problem?

## Slide 15
Host A
Src: A's MAC address
Dst: ff:ff:ff:ff:ff:ff
DHCPDISCOVER
Src: <Server MAC address>
Dst: ff:ff:ff:ff:ff:ff
DHCPOFFER:
Your IP: 192.168.1.102
Mask: 255.255.255.0
Router: 192.168.1.1
...
DHCP server
(More steps after this)

## Slide 16
Host A
Src: A's MAC address
Dst: ff:ff:ff:ff:ff:ff
DHCPDISCOVER
Src: <Server MAC address>
Dst: ff:ff:ff:ff:ff:ff
DHCPOFFER:
Your IP: 192.168.1.102
Mask: 255.255.255.0
Router: 192.168.1.1
...
DHCP server
(More steps after this)
=> Again, host needs to use broadcast address. Why?
=> Problem?

## Slide 17: Home routers
The good, the bad, and the ugly…

## Slide 18: What’s in a home router?

## Slide 19: Story time

## Slide 20: Routing

## Slide 21: Challenges in moving packets
Forwarding:
Routing:
Notes: Forwarding uses forwarding table, routing builds forwarding table

## Slide 22: Challenges in moving packets
Forwarding: given a packet, decide which interface to send the packet (based on IP destination)
Routing: network-wide process of determining a packet’s path through the network
  => How each router builds its forwarding table
Notes: Forwarding uses forwarding table, routing builds forwarding table

## Slide 23
Routing is the process of updating forwarding tables
  Routers exchange messages about networks they can reach

## Slide 24
Routing is the process of updating forwarding tables
  Routers exchange messages about networks they can reach
Goal: find optimal route (or any route…) for every other destination
This is a hard problem
  Decentralized
  Topology always changing
  Scale!

## Slide 25
Map of the Internet, 2021 (via BGP)
OPTE project
Routing is how we build this picture!

## Slide 26: How do we connect everything?
Relies on hierarchical nature of IP addressing
Smaller routers don’t need to know everything, just another router that knows more
  Has default route
Core routers know everything => no default!

## Slide 27: A forwarding table (my laptop)
deemer@ceres ~ % ip route
default via 10.3.128.1 dev wlp2s0
10.3.128.0/18 dev wlp2s0 proto dhcp scope link src 10.3.135.44 metric 3003
172.18.0.0/16 dev docker0 proto kernel scope link src 172.18.0.1
192.168.1.0/24 dev enp0s31f6 proto kernel scope link src 192.168.1.1

## Slide 28: A large table
rviews@route-server.ip.att.net>show route table inet.0 active-path
inet.0: 866991 destinations, 13870153 routes (866991 active, 0 holddown, 0 hidden)
+ = Active Route, - = Last Active, * = Both
0.0.0.0/0 *[Static/5] 5w0d 19:43:09
> to 12.0.1.1 via em0.0
1.0.0.0/24 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 3356 13335 I, validation-state: valid
> to 12.0.1.1 via em0.0
1.0.4.0/22 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 3356 4826 38803 I, validation-state: valid
> to 12.0.1.1 via em0.0
1.0.4.0/24 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 3356 4826 38803 I, validation-state: valid
> to 12.0.1.1 via em0.0
1.0.5.0/24 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 3356 4826 38803 I, validation-state: valid
> to 12.0.1.1 via em0.0
1.0.6.0/24 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 3356 4826 38803 I, validation-state: valid
> to 12.0.1.1 via em0.0
1.0.7.0/24 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 3356 4826 38803 I, validation-state: valid
> to 12.0.1.1 via em0.0
1.0.64.0/18 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 2497 7670 18144 I, validation-state: unknown
> to 12.0.1.1 via em0.0
1.0.128.0/17 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 3356 38040 23969 I, validation-state: unknown
> to 12.0.1.1 via em0.0
1.0.128.0/18 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 3356 38040 23969 I, validation-state: unknown
> to 12.0.1.1 via em0.0
1.0.128.0/19 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 3356 38040 23969 I, validation-state: unknown
> to 12.0.1.1 via em0.0
1.0.128.0/24 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 6939 4651 23969 I, validation-state: unknown
> to 12.0.1.1 via em0.0
1.0.129.0/24 *[BGP/170] 1d 10:24:47, localpref 100, from 12.122.83.238
AS path: 7018 6939 4651 23969 I, validation-state: unknown
> to 12.0.1.1 via em0.0
Notes: Takes this information and synthesizes it down into its forwarding table baed on interfaces

## Slide 29
At this scale, we think about routing to whole networks, i.e., some entity with some set of IP prefixes:
e.g. Brown University @ 128.148.0.0/16, 138.16.0.0/16

## Slide 30
At this scale, we think about routing to whole networks, i.e., some entity with some set of IP prefixes:
e.g. Brown University @ 128.148.0.0/16, 138.16.0.0/16
We call each entity an Autonomous System (AS):
a single administrative domain that lives on the Internet

## Slide 31
Routing is organized in two levels:
Intra-domain (interior) routing: routing within an AS
Inter-domain (exterior) routing: routing between ASes

## Slide 32
Routing is organized in two levels:
Intra-domain (interior) routing: routing within an AS
=> Full knowledge of the network inside the AS => One administrator, routing policy => Strive for optimal paths
Inter-domain (exterior) routing: routing between ASes
  => None of the above, decisions instead made by policy (later)
^ We are here today

## Slide 33: Intra-Domain (Interior) Routing

## Slide 34
Network == Graph
Assign cost to edges
=> latency, bandwidth, ….

## Slide 35
Network == Graph
Assign cost to edges
=> latency, bandwidth, ….

## Slide 36
Typically, view network as a graph
Nodes are routers
Assign some cost to each edge
  latency, b/w, queue length, …
Goal: find lowest-cost path between nodes
  Each node individually computes routes
Collect routes into a routing table, used to generate the forwarding table based on lowest-cost path

## Slide 37
Generally: routing algorithms are decentralized

## Slide 38
Generally: routing algorithms are decentralized
=>In general, no one entity telling routers what routes to use
=> Even for “interior” routing, where there is one admin, routers independently compute how to update their tables based on latest info from other routers

## Slide 39
Two classes of intra-domain routing algorithms
Distance Vector (Bellman-Ford shortest path algorithm)
Link State (Djikstra/Prim shortest path algorithm)

## Slide 40
Two classes of intra-domain routing algorithms
Distance Vector (Bellman-Ford shortest path algorithm)
  Idea: routers get updates from their neighbors
Link State (Djikstra/Prim shortest path algorithm)

## Slide 41: First type: Distance Vector Routing
Notes: Local routing algorithm

## Slide 42: Distance Vector Routing
Each node maintains a routing table
Exchange updates with neighbors about node’s links: => List of (Destination, Cost) pairs
Notes: Local routing algorithm

## Slide 43: Distance Vector Routing
Each node maintains a routing table
Exchange updates with neighbors about node’s links: => List of (Destination, Cost) pairs
When to send updates?
  Periodically (seconds to minutes)
  Whenever table changes (triggered update)
  Time out an entry if no updates within some time interval
Notes: Local routing algorithm

## Slide 44: Distance Vector Routing
Each node maintains a routing table
Exchange updates with neighbors about node’s links: => List of (Destination, Cost) pairs
When to send updates?
  Periodically (seconds to minutes)
  Whenever table changes (triggered update)
  Time out an entry if no updates within some time interval
Dest. | Cost | Next Hop
A | 3 | S
B | 4 | T
C | 5 | S
D | 6 | U
Notes: Local routing algorithm

## Slide 45: Distance Vector: Update rules
Say router R receives an update (D, cD) from neighbor N at cost CN
=> Know: R can reach D via N with cost c = cD + cN
How to update table?
If D not in table, add (D, c, N) (New route!)
If table has entry (D, M, cold):
  if c < cold: update table to (D, c, M). (Lower cost!)
  if c > cold and M == N: update table to (D, c, N) (Cost increased!)
  if c > cold and M != N: ignore (N is better)
  if c == cold and M ==N: no change (No new info)
(Just refresh timeout)

## Slide 46: DV Example

## Slide 47: DV Example
Dest. | Cost | Next Hop
(B) | (0) | (B)
A | 1 | A
C | 1 | C
D | 2 | C
E | 2 | A
F | 2 | A
G | 3 | A
B’s routing table

## Slide 48
Suppose router R has the following table:
What happens when it gets
this update from router S?
Dest. | Cost | Next Hop
A | 3 | S
B | 4 | T
C | 5 | S
D | 6 | U
Dest. | Cost
A | 2
B | 3
C | 5
D | 4
E | 2

## Slide 49
What happens when the D-A link fails?
A
B
C
D
Notes: D-A fails
A sends update to B: (D, Inf)
C sends an update to B, so it now has (D, 2,C) (This is the race)
B sends update to A, which gets (D, B, 4)
Keep going until you reach infinity

## Slide 50
What happens when the D-A link fails?
A
B
C
D
=> “Count to Infinity” problem
Notes: D-A fails
A sends update to B: (D, Inf)
C sends an update to B, so it now has (D, 2,C) (This is the race)
B sends update to A, which gets (D, B, 4)
Keep going until you reach infinity

## Slide 51
What happens when the D-A link fails?
A
B
C
D
Updates occur in a loop with increasing cost until cost reaches infinity (16)!
=> Count to infinity => long time to converge when links fail
Notes: D-A fails
A sends update to B: (D, Inf)
C sends an update to B, so it now has (D, 2,C) (This is the race)
B sends update to A, which gets (D, B, 4)
Keep going until you reach infinity

## Slide 53: Can we avoid loops?
Does IP TTL help? Nope.
Simple approach: consider a small cost n (e.g., 16) to be infinity

## Slide 54: Can we avoid loops?
Does IP TTL help? Nope.
Simple approach: consider a small cost n (e.g., 16) to be infinity
Fundamental problem: distance vector only based on local information!
=> Not enough info to resolve loops, race conditions, count-to-infinity,
but there are some tricks…

## Slide 55
RFC1058 (1988): The original RIP standard*
*: Obsoleted by RFC2453 (don’t use RFC 1058 for the project,
Use RFC 2453 instead)

## Slide 56
One strategy: Split Horizon
When sending updates to node A, don’t include routes you learned from A
Prevents B and C from sending cost 2 to A

## Slide 57
Split Horizon + Poison reverse
Rather than not advertising routes learned from A, explicitly include cost of ∞.
Faster to break out of loops, but increases advertisement sizes

## Slide 58
Split Horizon + Poison reverse
Rather than not advertising routes learned from A, explicitly include cost of ∞.
Faster to break out of loops, but increases advertisement sizes
=> Does it help?

## Slide 59
Split Horizon + Poison reverse
Rather than not advertising routes learned from A, explicitly include cost of ∞.
Faster to break out of loops, but increases advertisement sizes
Does it help? Not completely.
=> A common convention, might reduce time to converge, but overall hard to see effect vs. split horizon

## Slide 60
Even with split horizon + poison reverse,
can still create loops with >2 nodes!
A
B
C
D
Notes: You need to do triggered updates in the assignment

## Slide 61
Even with split horizon + poison reverse,
can still create loops with >2 nodes!
What else can we do?
A
B
C
D
Notes: You need to do triggered updates in the assignment

## Slide 62
Even with split horizon + poison reverse,
can still create loops with >2 nodes!
What else can we do?
Triggered updates: send update as soon as link state changes
Hold down: delay using new routes for certain time, affects convergence time
A
B
C
D
Notes: You need to do triggered updates in the assignment

## Slide 63: Practice
Routers A,B,C,D use RIP. When B sends a periodic update to A, what does it send…
When using standard RIP?
When using split horizon + poison reverse?
A
B
C
D
Dest. | Cost | Next Hop
A | 1 | A
C | 1 | C
D | 2 | A
B’s routing table

## Slide 64
From RFC2453, RIP v2 (1998):

## Slide 65: Link State Routing

## Slide 66: Link State Routing: The Alternative
Strategy: each router sends information about its neighbors to all nodes
Example: OSPF

## Slide 67: Link State Routing: The Alternative
Strategy: each router sends information about its neighbors to all nodes
Nodes build the full graph, not just neighbor info
Updates have more state info
Example: OSPF

## Slide 68: Link State Routing: The Alternative
Strategy: each router sends information about its neighbors to all nodes
Nodes build the full graph, not just neighbor info
  => Can define “areas” to scale this in large networks
Updates have more state info
  Node IDs, version info (sequence number, TTL), … => Can be used to detect loops, stale info
Focuses on building a consistent view of network state

## Slide 69: Link State Routing: how it works
Each node computes shortest paths from itself
How? Dijkstra’s algorithm
  Given: full graph of nodes
  Find best next hop to each other node

## Slide 70: Link State Routing: how it works
Each node computes shortest paths from itself
How? Dijkstra’s algorithm
  Given: full graph of nodes
  Find best next hop to each other node
Tradeoffs?

## Slide 71: Tradeoffs: Link State (LS) vs. Distance Vector (DV)
LS sends more messages vs. DV
LS requires more computation vs. DV
Convergence time
  DV: Varies (count-to-infinity)
  LS: Reacts to updates better
Robustness
  DV: Bad updates can affect whole network
  LS: Bad updates affect a single node’s update
=> RIP isn’t used in production environments anymore…

## Slide 72: Examples (and complexity)
Algorithm | Method | Pages in RFC
RIP v2 (RFC 2453) | Distance Vector | 38

## Slide 73: Examples (and complexity)
OSPF: Open Shortest Path First
IS-IS: OSI standard similar to OSPF, doesn’t depend on IP
Algorithm | Method | Pages in RFC
RIP v2 (RFC 2453) | Distance Vector | 38
OSPF (RFC 2328) | Link-State | 244
IS-IS (OSI) | Link-State | 210

## Slide 74
So why not just use OSPF everywhere?
Does it scale?

## Slide 75
Map of the Internet, 2021 (via BGP)
OPTE project
Not to this.

## Slide 76: Why not?
Can’t build a full routing graph with the whole Internet
More a policy problem than a technical problem

## Slide 77: Why not?
Can’t build a full routing graph with the whole Internet
More a policy problem than a technical problem
  No unified way to represent cost
  No single administrator
  Networks (ASes) have different policies on what “best” routes to choose
Need a different routing mechanism for exterior routing => BGP

## Slide 78
With BGP: we talk about routing to Autonomous Systems (ASes)
= > Generally, large networks advertise some set of IP prefixes to the Internet
=> Each AS has its own policy for how it does routing

## Slide 79
With BGP: we talk about routing to Autonomous Systems (ASes)
= > Generally, large networks advertise some set of IP prefixes to the Internet
=> Each AS has its own policy for how it does routing

## Slide 80: BGP: A Path Vector Protocol
Distance vector + extra information
  eg. “I can reach prefix 128.148.0.0/16 through ASes 44444 3356 14325 11078”

## Slide 81: BGP: A Path Vector Protocol
Distance vector + extra information
  For each route, router store the complete path (ASs)
  No extra computation, just extra storage (and traffic)
  BGP gets to decide what path to advertise to neighbors
  eg. “I can reach prefix 128.148.0.0/16 through ASes 44444 3356 14325 11078”

## Slide 82
  eg. “I can reach prefix 128.148.0.0/16 through ASes 44444 3356 14325 11078”
What would a loop look like?
Fun fact: loops are easy to avoid…

## Slide 83: BGP: A Path Vector Protocol
Distance vector + extra information
  For each route, router store the complete path (ASs)
  No extra computation, just extra storage (and traffic)
  BGP gets to decide what path to advertise to neighbors
BGP routers look at path to decide how to “propagate” route, based on policy
Can easily avoid loops!
  eg. “I can reach prefix 128.148.0.0/16 through ASes 44444 3356 14325 11078”

## Slide 84: BGP Implications
No loops!
Not all ASs know all paths
Reachability not guaranteed
  Decentralized combination of policies
Scaling
  74K ASs
  959K+ prefixes
  ASs with one prefix: 25K
  Most prefixes by one AS: 10008 (Uninet S.A. de C.V., MX)
Source: cidr-report 18Oct2022

## Slide 85: Why study BGP?
BGP is what makes the Internet run.
Lots of problems…

## Slide 86
A Network Operations Center (NOC)

## Slide 87: BGP Example

## Slide 88: BGP Example

## Slide 89: BGP Example

## Slide 90: BGP Example

## Slide 91: BGP Example

## Slide 92: Demo: AS11078

## Slide 93: Extra content

## Slide 94: … or does it?

## Slide 95: Where it gets weird…
For many end hosts:
(IP assigned to your host) != (Your ”public” IP)
(IP seen by other systems on the Internet)
Notes: Address sharing

## Slide 96: Where it gets weird…
You get just one IP from your ISP…
=> Need to share IP among many devices on the same network!
Notes: Address sharing

## Slide 97: Where it gets weird…
You get just one IP from your ISP…
=> Need to share IP among many devices on the same network!
=> Network Address Translation (NAT) (A form of connection multiplexing)
Solution: Create a “private” IP range used within local network
=> Routers need to do extra work to share public IP among many private IPs
Notes: Address sharing

## Slide 99: How NAT works
192.168.1.100
1.2.1.102
192.168.1.1
5.6.7.8
IF1
IF0
“Inside” network
192.168.1.0/24
192.168.1.101
Rest of Internet
S
Goal: Share one IP among many hosts on a private network
Router translates (modifies) packets from ”inside” to use “outside” address
(The most common type)

## Slide 100: Private IPs (RFC1918)
IP ranges reserved for “private” networks:
Prefix | Use
127.0.0.0/8 | “Loopback” address—always for current host
10.0.0.0/8 | Reserved for private internal networks (RFC1918)
192.168.0.0/16 | IF2
172.16.0.0/12 | IF0

## Slide 101: Private IPs (RFC1918)
IP ranges reserved for “private” networks:
Many networks will use these blocks internally
These IPs should never be routed over the Internet!
  What would happen if they were?
Prefix | Use
127.0.0.0/8 | “Loopback” address—always for current host
10.0.0.0/8 | Reserved for private internal networks (RFC1918)
192.168.0.0/16 | IF2
172.16.0.0/12 | IF0

## Slide 102: How NAT works
192.168.1.100
1.2.1.102
192.168.1.1
5.6.7.8
IF1
IF0
“Inside” network
192.168.1.0/24
192.168.1.101
Rest of Internet
S
=> Router needs to remember connection state
=> Router makes some (sketchy) assumptions about traffic
Goal: Share one IP among many hosts on a private network
Router translates (modifies) packets from ”inside” to use “outside” address
(The most common type)
Your “public” IP

## Slide 104
Where are the port numbers?????
IP Header

## Slide 105
UDP
TCP
… ports are actually part of the transport layer header!
Problem???????

## Slide 106
UDP
TCP
… ports are actually part of the transport layer header!
Problem?
Technically a violation of layering! Network layer shouldn’t care about port numbers, but here it matters
NAT needs to know semantics of TCP/UDP (how connections start/end…
...but wait there’s more…

## Slide 107: NAT vs. Snowcast

## Slide 108
192.168.1.100
1.2.1.102
192.168.1.1
5.6.7.8
IF1
IF0
“Inside” network
192.168.1.0/24
192.168.1.101
Rest of Internet
S
What happens when outside host S wants to connect to inside host A?
A
B
C
R

## Slide 109
192.168.1.100
1.2.1.102
192.168.1.1
5.6.7.8
IF1
IF0
“Inside” network
192.168.1.0/24
192.168.1.101
Rest of Internet
S
Can’t do it (at least without special setup)!
By default, R only knows how to translate packets for connections originating from INSIDE the network
Breaks end to end connectivity!!!
What happens when outside host S wants to connect to inside host A?
A
B
C
R

## Slide 110
192.168.1.100
1.2.1.102
192.168.1.1
5.6.7.8
IF1
IF0
“Inside” network
192.168.1.0/24
192.168.1.101
Rest of Internet
S
Can’t do it (at least without special setup)!
By default, R only knows how to translate packets for connections originating from INSIDE the network
Breaks end to end connectivity!!!
What happens when outside host S wants to connect to inside host A?
A
B
C
R

## Slide 111: End to end connectivity, you say?

## Slide 112: Why is this bad?
NAT is used in just about every consumer network
Generally: can’t connect directly to an end host unless it connects to you first

## Slide 113: Why is this bad?
NAT is used in just about every consumer network
Generally: can’t connect directly to an end host unless it connects to you first
Need extra work for any protocols that need a direct connection between hosts
=> When do we need this?

## Slide 114: Why is this bad?
NAT is used in just about every consumer network
Generally: can’t connect directly to an end host unless it connects to you first
Need extra work for any protocols that need a direct connection between hosts
Protocols that aren’t strictly client-server
Latency critical applications: voice/video calls, games

## Slide 115: NAT Traversal
Various methods, depending on the type of NAT
Examples:
Manual method: port forwarding
ICE: Interactive Connectivity Establishment (RFC8445)
STUN: Session Traversal Utilities for NAT (RFC5389)
One idea: connect to external server via UDP, it tells you the address/port