## Slide 1: CSCI-1680 Transport Layer I
Nick DeMarinis
Based partly on lecture notes by Rodrigo Fonseca, David Mazières, Phil Levis, John Jannotti

## Slide 2: Administrivia
IP: due tonight!
  Look for email today/tomorrow about grading meetings + required post-project survey

## Slide 3: Administrivia
IP: due tonight!
  Look for email today/tomorrow about grading meetings + required post-project survey
“Between the time you’ve handed in and the demo meeting, you can continue to making small changes and bug fixes and push them to your git repo/Gradescope”
  OK: Fixing bugs, code cleanup, README
  Not OK: Implementing RIP, adding new features

## Slide 4: Administrivia
HW2 is out (finally!): Due Monday, Oct 28
HW3 will be super short
TCP: Handout out tomorrow, stencil/repo setup over weekend
  Gearup on Thursday, Oct 24 6-8pm in CIT 368

## Slide 5: Warmup
You capture the following packets on your router. How many unique connections are present?
Pkt# | Source | Local | Destination | 
 | IP | Port | IP | Port
P1 | 10.0.0.1 | 12345 | 1.2.3.4 | 80
P2 | 10.0.0.2 | 55444 | 5.6.7.8 | 443
P3 | 1.2.3.4 | 80 | 10.0.0.1 | 12345
P4 | 10.0.0.1 | 43233 | 1.2.3.4 | 80

## Slide 6: Today
Light overview of the transport layer and TCP
  Why we need TCP
  What components are involved
  What you will do in the project

## Slide 7
Transport layer: the story so far
  Provides support for different applications via ports
  OS provides interface to applications via sockets
For now: transport layer is part of OS, service provided to apps

## Slide 8: The headers
UDP
TCP
Port numbers are part of these headers
=> OS uses these to map to sockets

## Slide 9
Motivation: sending a big file
$ cp ~/dir/all-my-files.zip ~/some-other-dir
A problem, in pseudocode:
What are some challenges with implementing the network part?
$ scp ~/dir/all-my-files.zip 1.2.3.4:/some-other-dir

## Slide 10
Motivation: sending a big file
func sender() {
fd, _ := os.Open("all-my-files.zip")
conn, _ := net.Dial("1.2.3.4:80")
buf := ReadTheWholeFile(fd)
conn.Write(buf)
}
A problem, in pseudocode:
What are some challenges with implementing the network part?
func receiver() {
conn, err := net.Listen(“:80”)
buf := make([]byte, . . .)
conn.Read(buf)
fd = os.Open(”copy-of-files.zip”)
fd.Write(buf)
}

## Slide 11
Motivation: sending a big file
func sender() {
fd, _ := os.Open("all-my-files.zip")
conn, _ := net.Dial("1.2.3.4:80")
buf := ReadTheWholeFile(fd)
conn.Write(buf)
}
A problem, in pseudocode:
func receiver() {
conn, err := net.Listen(“:80”)
buf := make([]byte, . . .)
conn.Read(buf)
fd = os.Open(”copy-of-files.zip”)
fd.Write(buf)
}
How do we get data from A->B, reliably?

## Slide 12
What features do we need?

## Slide 13
UDP: User Datagram Protocol
Send a message between ports… and nothing else

## Slide 14
Map of the Internet, 2021 (via BGP)
OPTE project
UDP: What could possibly go wrong?

## Slide 15: Problem: Reliability
Packets could…
Dropped packets
Duplicate packets
Packets arrive out of order
Multiple hops and paths => Lots of opportunities for failure!
=> TCP has mechanisms to deal with this

## Slide 16
Also: performance challenges
Hosts have different (and unknown!) resources
Network has unknown resources
  => Varying RTT, link bandwidth

## Slide 17
Also: performance challenges
Hosts have different (and unknown!) resources
=> Flow control: how much data can we send to receiver?
Network has unknown resources
  => Varying RTT, link bandwidth
  => Congestion control: must not overload network

## Slide 18
Also: performance challenges
Hosts have different (and unknown!) resources
=> Flow control: how much data can we send to receiver?
Network has unknown resources
  => Varying RTT, link bandwidth
  => Congestion control: must not overload network
Two performance goals:
1. Must not overwhelm receiver, or network (critical!!)
2. Maximize throughput => best performance

## Slide 19: Transport Layer Reliability
Extra difficulties
  Multiple hops
  Multiple potential paths
What does this mean?
  Multiple opportunities for failure
  Hosts have different resources
  Varying RTTs
Notes:     Both across connections and during a connection
    Why do they vary? What do they influence?
RTT influences the potential window size (delay X bandwidth), the values for timeouts.

## Slide 20: Extra Difficulties (cont.)
Out of order packets
  Not only because of drops/retransmissions
  Can get very old packets (up to 120s), must not get confused
Unknown resources at other end
  Must be able to discover receiver buffer: flow control
Unknown resources in the network
  Should not overload the network
  But should use as much as safely possible to maximize throughput
Notes: We call this congestion control

## Slide 21
So how does it work?

## Slide 22
TCP: the big picture

## Slide 23: TCP – Transmission Control Protocol
Service model: “reliable, connection oriented, full duplex ordered byte stream”
Flow control: If one end stops reading, writes at other eventually stop/fail
Congestion control: Keeps sender from overloading the network

## Slide 24: TCP: Key features
RFC 793 (1981) (+ many others now)
Creates concept of connections between two endpoints
=> Each connection has its own state
Notes: Don’t always need reliability!

## Slide 25: TCP: Key features
Initially: RFC 793 (1981) (+ many others now)
Creates concept of connections between two endpoints
=> Each connection has its own state
End-to-end protocol
Notes: Don’t always need reliability!

## Slide 26: From Lec 2: OSI Model
Application Protocol
Transport Protocol
Network Protocol
Link-Layer Protocol
Notes: Open Systems Interconnect, ISO
We no longer care about paths

## Slide 27: From Lec 2: OSI Model
Application Protocol
Transport Protocol
Network Protocol
Link-Layer Protocol
New abstraction: builds on network layer
=> Just care about endpoint, not individual routers on path
=> All mechanisms run on endpoints (not routers) => Why?
Notes: Open Systems Interconnect, ISO
We no longer care about paths

## Slide 28: Why not provide X on the network layer?
X = Reliability, security, message ordering…
Might be too costly
  Extra features aren’t free: don’t burden protocols that don’t need them!
  Cost could be extra latency, extra computation, …
Features might be conflicting
  Timeliness vs. in-order delivery
Might not be enough
  Example: reliability
Notes: Insufficient: need an end-to-end picture to get reliable delivery

## Slide 29: End-to-end argument
Functions placed at lower levels of a system may be redundant or of little value
  They may need to be performed at a higher layer anyway
But they may be justified for performance reasons
  Or just because they provide most of what is needed
  Example: retransmissions
=> Takeaway: Important to weigh the costs and benefits at each layer!
Notes: Example: Bit-torrent file transfer
Example performance enhancement
o-----o-----o----o 0.1 chance of drop
End-to-end ack: (0.9^4)^2 = 0.43 (~2.3X)
2 Retransmissions per hop:
Failure: fails three retransmissions = ((1-(0.1)^3)^4)^8 = 0.99

## Slide 30: TCP Header

## Slide 31: Important Header Fields
Ports: multiplexing
Sequence number
  Where segment is in the stream (in bytes)
Acknowledgment Number
  Next expected sequence number
Window
  How much data you’re willing to receive
Flags…

## Slide 32: Important Header Fields: Flags
SYN:
ACK:
FIN:
RST: reset connection (used for errors)
PSH: push data to the application immediately
URG: whether there is urgent data

## Slide 33: Important Header Fields: Flags
SYN: establishes connection (“synchronize”)
ACK: this segment ACKs some data (all packets except first)
FIN: close connection (gracefully)
RST: reset connection (used for errors)
PSH: push data to the application immediately
URG: whether there is urgent data

## Slide 34: Less important header fields
Checksum: Very weak, like IP
  Has weird semantics (”pseudo header”), more on this later…
Data Offset: used to indicate TCP options (mostly unused)
Urgent Pointer

## Slide 35: TCP Standards: The Many RFCs

## Slide 36: TCP Standards: The Many RFCs
RFC793 (Original)

## Slide 37: TCP Standards: The Many RFCs
RFC793 (Original)
RFC1122 (Some corrections)

## Slide 38: TCP Standards: The Many RFCs
RFC793 (Original)
RFC1122 (Some corrections)
RFC5681 (Congestion control)

## Slide 39: TCP Standards: The Many RFCs
RFC793 (Original)
RFC1122 (Some corrections)
RFC5681 (Congestion control)
RFC7414 (Roadmap to TCP RFCs)

## Slide 40: TCP Standards: The Many RFCs
RFC793 (Original)
RFC1122 (Some corrections)
RFC5681 (Congestion control)
Various Errata . . .
RFC7414 (Roadmap to TCP RFCs)

## Slide 41: TCP Standards: The Many RFCs

## Slide 42
RFC9293
The One RFC

## Slide 43: Establishing a Connection
Goals
Contact the other side (or error)
Both sides agree on initial sequence numbers

## Slide 44: Establishing a Connection
Three-way handshake
  Two sides agree on respective initial sequence nums
If no one is listening on port: OS may send RST
If server is overloaded: ignore SYN
If no SYN-ACK: retry, timeout
listen(),
accept()
accept()
returns
connect()

## Slide 45: Summary of TCP States
Passive close:
Can still send!
Active close:
Can still receive
Connection Establishment

## Slide 46: TCP State Diagram

## Slide 47: Sequence numbers
How to pick the initial sequence number?
Protocols based on relative sequence numbers based on starting value
Why not start at 0?
RFC9293, Sec 3.4.1: Procedure for picking ISN, based on timer and cryptographic hash
  => For project, just pick a random integer :)

## Slide 48: Relative Sequence Numbering

## Slide 49
How do we tell two connections apart?
=> Port numbers
  5-tuple (proto., source IP, source port, dest IP, dest port) => 1 Connection
  Kernel maintains socket table: maps (5-tuple) => Socket
If a 5-tuple is reused => new ISN, so sequence numbers likely out of range from past connection

## Slide 50: Netstat
deemer@vesta ~/Development % netstat -an
Active Internet connections (including servers)
Proto Recv-Q Send-Q Local Address Foreign Address (state)
tcp4 0 0 10.3.146.161.51094 104.16.248.249.443 ESTABLISHED
tcp4 0 0 10.3.146.161.51076 172.66.43.67.443 ESTABLISHED
tcp6 0 0 2620:6e:6000:900.51074 2606:4700:3108::.443 ESTABLISHED
tcp4 0 0 10.3.146.161.51065 35.82.230.35.443 ESTABLISHED
tcp4 0 0 10.3.146.161.51055 162.159.136.234.443 ESTABLISHED
tcp4 0 0 10.3.146.161.51038 17.57.147.5.5223 ESTABLISHED
tcp6 0 0 *.51036 *.* LISTEN
tcp4 0 0 *.51036 *.* LISTEN
tcp4 0 0 127.0.0.1.14500 *.* LISTEN
Notes: If you get a packet from X:Y---it goes to this socket

## Slide 51: Keeping state: the TCB
State for a TCP connection kept in Transmission Control Buffer (TCB)
Keeps initial sequence numbers, connection state, send/recv buffers, status of unACK’d segments, …
When to allocate?
  Server: listening on a connection*
  Client: Initiating a connection (sending a SYN)
  Server: accepting a new connection (receiving SYN)
Notes: Listening sockets won’t use all of the TCB state

## Slide 52: Recall: the socket table
Each connection has an associated TCB in the kernel
For each packet, kernel maps the 5-tuple (tcp/udp, local IP, local port, remote IP, remote port) => socket
Depending on socket type, socket contains TCB
deemer@vesta ~ % netstat -anl
Active Internet connections (including servers)
Proto Recv-Q Send-Q Local Address Foreign Address (state)
tcp4 0 0 172.17.48.121.56915 192.168.1.58.7000 SYN_SENT
tcp4 0 0 172.17.48.121.56908 142.250.80.35.443 ESTABLISHED
tcp4 0 0 172.17.48.121.56887 13.225.231.50.80 ESTABLISHED
. . .
tcp4 0 0 *.22 *.* LISTEN
Notes: You will implement this

## Slide 53
Two “types” of sockets:
“Normal” sockets
Listen sockets
deemer@vesta ~ % netstat -anl
Active Internet connections (including servers)
Proto Recv-Q Send-Q Local Address Foreign Address (state)
tcp4 0 0 172.17.48.121.56915 192.168.1.58.7000 SYN_SENT
tcp4 0 0 172.17.48.121.56908 142.250.80.35.443 ESTABLISHED
tcp4 0 0 172.17.48.121.56887 13.225.231.50.80 ESTABLISHED
. . .
tcp4 0 0 *.22 *.* LISTEN

## Slide 54
“Normal” sockets
  Connection between two specific endpoints
  Can send/recv data
Listen sockets
  Created by receiver to accept new connections
  When a client connects, client info gets queued by kernel
  When server process calls accept(), a new (”normal”) socket is created between the server and that client
Proto Recv-Q Send-Q Local Address Foreign Address (state)
tcp4 0 0 172.17.48.121.56887 13.225.231.50.80 ESTABLISHED
. . .
tcp4 0 0 *.22 *.* LISTEN

## Slide 55
RFC 9293, Sec 3.3.2

## Slide 56: SYN flooding
What happens if you send a someone huge number of SYN packets?

## Slide 57: A hacky solution: SYN cookies
Don’t allocate TCB on first SYN
Encode some state inside the initial sequence number that goes back to the client (in the SYN+ACK)
What gets encoded?
  Coarse timestamp
  Hash of connection IP/port
  Other stuff (implementation dependent)
Better ideas?

## Slide 58: Next class
Sending data over TCP

## Slide 59: Connection Termination
FIN bit says no more data to send
  Caused by close or shutdown
  Both sides must send FIN to close a connection
Typical close
FIN
ACK
FIN
ACK
Close
Close
FIN_WAIT_1
CLOSE_WAIT
FIN_WAIT_2
LAST_ACK
TIME_WAIT
CLOSED
CLOSED
…
2MSL

## Slide 60: The IPv4 Header
Defined by RFC 791
RFC (Request for Comment): defines network standard
Notes: The key parts are HERE